## Slide 1: Ambient Backscatter
Vincent Liu
Aaron Parks, Vamsi Talla,
Shyam Gollakota, David Wetherall, Joshua Smith

## Slide 2: Our Goal
Interactive devices that compute and communicate without batteries

## Slide 3: What We Are After
How to power computation, sensing,
and communication?

## Slide 4: Leverage Existing Wireless Signals
TV
Cellular
Wi-Fi
Available at almost any time and place, rain or shine

## Slide 5: Recent Work Harvests 10s of μW [‘09]
Enough for computation and sensing
Orders of magnitude less power than needed for radio communication [‘13]

## Slide 6: Challenge: Communication Between Battery-Free Devices
Generating radio signals is expensive
Could duty cycle
  Limits interactive applications
  Can we communicate without
  either device generating radio signals?

## Slide 7: Ambient Backscatter
Alice
Bob
‘0’ bit – Absorb TV Signals
‘1’ bit – Reflect TV signals
TV Tower
Reception
Unaffected
Use existing signals instead of generating our own
Additional
Multipath
Works with only ~5% of the harvested power!

## Slide 8: Challenges

## Slide 9
Ambient Backscatter
Reader sends constant wave
Receive chain: 100s of mW
Reader centrally coordinates
RFID
Reader
Tag
Chart: 

## Slide 10
Tag
Tag
Ambient Backscatter
Uses uncontrollable signals
Receive chain: 0.5 μW
Need distributed MAC
Chart: 
Reader
Tag
Reader sends constant wave
Receive chain: 100s of mW
Reader centrally coordinates
Chart: 
RFID

## Slide 11: Challenges
Extracting backscattered signals from ambient signals we don’t control
Decoding on a battery-free device
Designing distributed MAC for battery-free devices

## Slide 12: Challenges
Extracting backscattered signals from ambient signals we don’t control
Decoding on a battery-free device
Designing distributed MAC for battery-free devices

## Slide 13: How Do We Extract The Backscattered Signals?
Case 1: Alice absorbs
At Bob: TV signal
Case 2: Alice reflects
At Bob: TV signal
+ Weak Reflection
Alice’s reflections change the average amplitude
Alice
Bob
TV Tower

## Slide 14: Solution: Detect Changes in Average Amplitude
Chart: 
Chart: 
Chart: 
Chart: 
Alice Sends 1010…
Alice Inactive
Moving Window Average

## Slide 15
If we had digital samples, averaging would be easy
Need power-hungry analog-to-digital converters

## Slide 16: Challenges
Extracting backscattered signals from ambient signals we don’t control
Decoding on a battery-free device
Designing distributed MAC for battery-free devices

## Slide 17: Use RC Circuits to Average
Capacitor slowly charges/discharges when voltage is applied/removed
Provides a cheap, analog,
exponential moving average
R
C
Chart: 
Chart: 

## Slide 18: Use RC Circuits to Average
R
C
Capacitor slowly charges/discharges when voltage is applied/removed
Provides a cheap, analog,
exponential moving average
Chart: 
By picking the right RC values,
we can selectively filter out the high TV frequencies
Chart: 

## Slide 19: Now that we can decode bits…
Physical Layer
Link Layer
Distributed MAC?

## Slide 20: Challenges
Extracting backscattered signals from ambient signals we don’t control
Decoding on a battery-free device
Designing distributed MAC for battery-free devices

## Slide 21: We Use CSMA
CSMA uses carrier sense, i.e. energy detection
Battery-free devices do not have energy levels
  Requires power-hungry ADCs
  Challenge: Energy detection
  without access to the energy levels

## Slide 22: Solution: Leverage Hardware Properties for Energy Detection
RC circuit filters out the TV signals  Removes high-amplitude variations
Hardware elements have a threshold  Low-amplitudes don’t change output
Chart: 
Chart: 
Constant Output
In the absence of backscattering,
we see a constant output

## Slide 23: Solution: Leverage Hardware Properties for Energy Detection
No backscatter  See all 0s or all 1s
Backscatter  See many transitions
Use bit transitions as proxy for
energy detection

## Slide 24: Evaluation

## Slide 25: Prototype Using Off-the-Shelf Components
Battery-free
Harvests and backscatters TV signals at 539 MHz
Microcontroller performs computation
LEDs
Touch Sensors

## Slide 26: Tested Locations
Seattle area with a 1MW TV tower at 539 MHz
Indoor and outdoor environments
Distances up to 10.5 km from the TV tower
  TV power ranged between -24dBm and -8dBm

## Slide 27: What Bit Rates Can We Achieve?
Three bit rates: 10kbps, 1kbps, 100bps
BER versus distance between two devices
Distance

## Slide 28: What Bit Rates Can We Achieve?
Chart: Distance Between Tags (ft)
| 0.49 | 0.82 | 1.15 | 1.48 | 1.8 | 2.13 | 2.46 | 2.79 | 3.12 | 3.44
100 bps | 0.0001 | 0.004 | 0.01 | 0.07
1 kbps | 0.0001 | 0.0225 | 0.0903 | 0.229 | 0.3446
10 kbps | 0.0001 | 0.00175 | 0.09156 | 0.0771 | 0.14929 | 0.13839 | 0.08661 | 0.12947 | 0.23305
100 bps
10 kbps
1 kbps
These results show the feasibility
of Ambient Backscatter

## Slide 29: Applications

## Slide 30: Identifying Misplaced Items
With ambient backscatter, devices can figure out they are misplaced on their own
We built a preliminary system with cereal boxes
In Grocery stores or Warehouses (e.g., Amazon)

## Slide 31: Identifying Misplaced Items
In Grocery stores or Warehouses (e.g., Amazon)
Works even if not all tags are in range of a reader

## Slide 32: Conclusion
We develop
  The first primitive that enables communication without either device generating RF signals
  A battery-free hardware prototype that computes and communicates using only TV signals
We transform existing signals into both a power source and a communication medium
  Opens up new research opportunities
abc.cs.washington.edu