## Slide 1: F10: A Fault-Tolerant Engineered Network
Vincent Liu, Daniel Halperin,
Arvind Krishnamurthy, Thomas Anderson
University of Washington

## Slide 2: Today’s Data Centers
Today’s data centers are built using multi-rooted trees
Commodity switches for cost, bisection bandwidth, and resilience to failures
*From Al-Fares et al.
SIGCOMM ‘08

## Slide 3: FatTree Example: PortLand
Heartbeats to detect failures
Centralized controller installs updated routes
Exploits path redundancy

## Slide 4: Unsolved Issues with FatTrees
Slow Detection
  Commodity switches fail often
  Not always sure they failed (gray/partial failures)
Slow Recovery
  Failure recovery is not local
  Topology does not support local reroutes
Suboptimal Flow Assignment
  Failures result in an unbalanced tree
  Loses load balancing properties

## Slide 5: F10
Co-design of topology, routing protocols and failure detector
  Novel topology that enables local, fast recovery
  Cascading protocols for optimal recovery
  Fine-grained failure detector for fast detection
Same # of switches/links as FatTrees

## Slide 6: Outline
Motivation & Approach
Topology: AB FatTree
Cascaded Failover Protocols
Failure Detection
Evaluation
Conclusion

## Slide 7: Why is FatTree Recovery Slow?
Lots of redundancy on the upward path
Immediately restore connectivity at the point of failure
dst
src

## Slide 8: Why is FatTree Recovery Slow?
No redundancy on the way down
Alternatives are many hops away
dst
src
src
No direct path
Has alternate path

## Slide 9: Type A Subtree
x
y
1
2
3
4
Consecutive Parents

## Slide 10: Type B Subtree
x
y
1
2
3
4
Strided Parents

## Slide 11: AB FatTree

## Slide 12: Alternatives in AB FatTrees
More nodes have alternative, direct paths
One hop away from node with an alternative
dst
src
src
No direct path
Has alternate path

## Slide 13: Cascaded Failover Protocols
A local rerouting mechanism
  Immediate restoration
A pushback notification scheme
  Restore direct paths
An epoch-based centralized scheduler
  globally re-optimizes traffic
μs
ms
s

## Slide 14: Local Rerouting
Route to a sibling in an opposite-type subtree
Immediate, local rerouting around the failure
dst
u

## Slide 15: Local Rerouting – Multiple Failures
Resilient to multiple failures, refer to paper
Increased load and path dilation
dst
u

## Slide 16: Pushback Notification
Detecting switch broadcasts notification
Restores direct paths, but not finished yet
u
No direct path
Has alternate path
u

## Slide 17: Centralized Scheduler
Related to existing work (Hedera, MicroTE)
Gather traffic matrices
Place long-lived flows based on their size
Place shorter flows with weighted ECMP

## Slide 18: Outline
Motivation & Approach
Topology: AB FatTree
Cascaded Failover Protocols
Failure Detection
Evaluation
Conclusion

## Slide 19: Why are Today’s Detectors Slow?
Based on loss of multiple heartbeats
  Detector is separated from failure
Slow because:
  Congestion
  Gray failures
  Don’t want to waste too many resources

## Slide 20: F10 Failure Detector
Look at the link itself
  Send traffic to physical neighbors when idle
  Monitor incoming bit transitions and packets
  Stop sending and reroute the very next packet
Can be fast because rerouting is cheap

## Slide 21: Outline
Motivation & Approach
Topology: AB FatTree
Cascaded Failover Protocols
Failure Detection
Evaluation
Conclusion

## Slide 22: Evaluation
Can F10 reroute quickly?
Can F10 avoid congestion loss that results from failures?
How much does this effect application performance?

## Slide 23: Methodology
Testbed
  Emulab w/ Click implementation
  Used smaller packets to account for slower speed
Packet-level simulator
  24-port 10GbE switches, 3 levels
  Traffic model from Benson et al. IMC 2010
  Failure model from Gill et al. SIGCOMM 2011
  Validated using testbed

## Slide 24: F10 Can Reroute Quickly
F10 can recover from failures in under a millisecond
Much less time than a TCP timeout

## Slide 25: F10 Can Avoid Congestion Loss
PortLand has 7.6x the congestion loss of F10 under realistic traffic and failure conditions

## Slide 26: F10 Improves App Performance
Median speedup is 1.3x
Speedup of a MapReduce computation

## Slide 27: Conclusion
F10 is a co-design of topology, routing protocols, and failure detector:
  AB FatTrees to allow local recovery and increase path diversity
  Pushback and global re-optimization restore congestion-free operation
Significant benefit to application performance on typical workloads and failure conditions
Thanks!