## Slide 1: Full-duplex Backscatter for <1 μW
Vincent Liu
Vamsi Talla, Shyam Gollakota

## Slide 2: Why Is This Hard?
Existing solutions require O(1W)
1,000,000x too much!

## Slide 3: Full-duplex Backscatter
First full-duplex design for battery-free devices
  Same frequency, single antenna

## Slide 4: Full-duplex Backscatter
RF source
Data (1 kbps)
Bob
Feedback (100 bps)
Alice
Brings self-interference down to the noise floor using < .75 uW

## Slide 5: Why Do We Care? Energy Is The Bottleneck!
Capacitor charging is exponential in time
Chart: Time
Column1 | 99.3511 | 91.6052 | 87.1376 | 82.8878 | 78.8453 | 75 | 71.3422 | 67.8628 | 64.5531 | 61.4048 | 58.4101 | 55.5614 | 52.8516 | 50.274 | 47.8221 | 45.4898 | 43.2712 | 41.1609 | 39.1534 | 37.2439 | 35.4275 | 33.6997 | 32.0561 | 30.4927 | 29.0056 | 27.591 | 26.2453 | 25
Threshold to
transmit a packet
Recovery from collisions and errors takes a long time

## Slide 6: Why Do We Care? Energy Is The Bottleneck!
Full-duplex can help fix this problem
Instantaneous feedback enables a better network
  Collision detection (100x recharge time reduction)
  Error correction (10x overhead reduction for every packet)

## Slide 7
How do we get full-duplex on battery-free devices?
How do we use instantaneous feedback to design a power-efficient network stack?

## Slide 8
How do we get full-duplex on battery-free devices?
How do we use instantaneous feedback to design a power-efficient network stack?

## Slide 9: Backscatter Overview
Alice
Bob
RF Source
Chart: Time
Alice absorbs:
Existing signal
Alice reflects:
Existing signal
& Reflection

## Slide 10: Challenge: Bob’s Reflections Lose Information
Chart: Time
Series 4 | 0 | 200
Alice
Bob
Alice absorbs:
Existing signal
Alice reflects:
Existing signal
& Reflection
Bob absorbs
Bob reflects
RF Source

## Slide 11: Solution: Change Phase Instead
Bob sends ‘0’:
Existing signal
& θ shift
Bob sends ‘1’:
Existing signal
& -θ shift
Chart: Time
Series 4 | 0 | 200
Bob absorbs
Bob reflects
Alice
Bob
RF Source
Bob can decode Alice’s signal
Alice can decode Bob’s signal

## Slide 12
Practically, phase modulation is imperfect
Residual interference

## Slide 13: Solution: Leverage Difference in Rates to Eliminate Residual Interference
Remove interference with high-pass filter
Remove interference with low-pass filter
Can be done with cheap, passive circuits at
NO additional power
Data (1 kbps)
Bob
Feedback (100 bps)
Alice

## Slide 14: Is Our Cancellation Effective?
Reduces self-interference to noise floor
Chart: Frequency (Hz)

## Slide 15
How do we get full-duplex on battery-free devices?
How do we use instantaneous feedback to design a power-efficient network stack?

## Slide 16: Challenge: Energy Is the Bottleneck
  Recovery from collisions/errors takes a long time
We use Full-duplex Backscatter to achieve instantaneous feedback

## Slide 17: Protocol: Acknowledge Data at a Bit Level
Split packet into 40-bit chunks
Receiver returns a checksum of each chunk
Sender verifies checksum
1
2
3
4
5
1
2
3
4
5
Forward data
channel
Feedback
channel
40 bits
4 bits
Time

## Slide 18: Does Full-duplex Help With Collisions?
Chart: Input Power (dBm)
| 3.31 | 2.31 | 1.31 | 0.31 | -0.69 | -1.69 | -2.69 | -3.69 | -4.689999999999999 | -5.689999999999999
Full-duplex Backscatter | 0.068856 | 0.092851 | 0.11163 | 0.14382 | 0.19931 | 0.28457 | 0.37849 | 0.59964 | 0.95389 | 2.9689
Conventional | 6.9305 | 9.3392 | 11.2188 | 14.4262 | 19.9043 | 28.3012 | 37.2792 | 58.5627 | 90.6699 | 240.5055
64-byte packet size
100x improvement in recharge time
Detect collisions and stop transmissions

## Slide 19: Does Full-duplex Help With Error Correction?
Chart: Bit Error Rate
| 0.0001 | 0.0002 | 0.0003 | 0.0004 | 0.0005 | 0.0006 | 0.0007 | 0.0008 | 0.0009 | 0.001 | 0.0011 | 0.0012 | 0.0013 | 0.0014 | 0.0015 | 0.0016 | 0.0017 | 0.0018 | 0.0019 | 0.002 | 0.0021 | 0.0022 | 0.0023 | 0.0024 | 0.0025 | 0.0026 | 0.0027 | 0.0028 | 0.0029 | 0.003 | 0.0031 | 0.0032 | 0.0033 | 0.0034 | 0.0035 | 0.0036 | 0.0037 | 0.0038 | 0.0039 | 0.004 | 0.0041 | 0.0042 | 0.0043 | 0.0044 | 0.0045 | 0.0046 | 0.0047 | 0.0048 | 0.0049
Full-duplex Backscatter | 0.47096 | 0.94386 | 1.4187 | 1.8955 | 2.3743 | 2.855 | 3.3377 | 3.8224 | 4.309 | 4.7977 | 5.2884 | 5.7811 | 6.2758 | 6.7726 | 7.2714 | 7.7723 | 8.2752 | 8.7802 | 9.2873 | 9.7964 | 10.3077 | 10.821 | 11.3365 | 11.8541 | 12.3738 | 12.8957 | 13.4197 | 13.9459 | 14.4743 | 15.0048 | 15.5375 | 16.0724 | 16.6095 | 17.1488 | 17.6904 | 18.2341 | 18.7802 | 19.3284 | 19.879 | 20.4318 | 20.9869 | 21.5442 | 22.1039 | 22.6659 | 23.2302 | 23.7968 | 24.3658 | 24.9371 | 25.5108
Conventional | 5.2536 | 10.7838 | 16.6051 | 22.733 | 29.1835 | 35.9738 | 43.1218 | 50.6462 | 58.5671 | 66.9053 | 75.6828 | 84.9229 | 94.65 | 104.8898 | 115.6694 | 127.0173 | 138.9635 | 151.5396 | 164.779 | 178.7166 | 193.3894 | 208.8362 | 225.0979 | 242.2177 | 260.2409 | 279.2152 | 299.1909 | 320.2211 | 342.3615 | 365.6707 | 390.2108 | 416.0467 | 443.247 | 471.8841 | 502.0338 | 533.7762 | 567.1958 | 602.3812 | 639.4259 | 678.4285 | 719.4926 | 762.7274 | 808.2478 | 856.175 | 906.6364 | 959.7664 | 1015.7064 | 1074.6052 | 1136.6197
>90% decrease in overhead
64-byte packet size
Recover from errors by retransmitting only the failed bits

## Slide 20: Conclusion
We show
  The first full-duplex design for battery-free devices
  A power-efficient network stack that has significant gains across the board
Re-design networking primitives with power as a first-class citizen
  MIMO (SIGCOMM’14), coding (SIGCOMM’14), UWB (?), TCP/IP (?), …