## Slide 1: Subways: A Case for Redundant, Inexpensive Data Center Edge Links
Vincent Liu, Danyang Zhuo, Simon Peter,
Arvind Krishnamurthy, Thomas Anderson
University of Washington

## Slide 2: Data Centers Are Growing Quickly
Data center networks need to be scalable
Upgrades need to be incrementally deployable
What’s worse: workloads are often bursty

## Slide 3: Today’s Data Center Networks
Oversubscribed: can send more than the network can handle
  Locality within a rack and/or cluster
Capacity upgrades are often “rip-and-replace”
Top-of-Rack (ToR)
Switches
Cluster
Switches
Racks of Servers
Cluster
Fabric
Switches

## Slide 4
Could we upgrade by augmenting servers
with multiple links?

## Slide 5: Strawman: Trunking
Add a parallel connection
Requires rewiring of existing links

## Slide 6: Strawman: Trunking
Add a parallel connection
Requires rewiring of existing links

## Slide 7: Subways
Instead of having all links go to the same ToR, use an overlapping pattern

## Slide 8: Advantages of Subways
Incremental upgrades
Short paths to more nodes
  Less traffic in the network backbone
Better statistical multiplexing
  A more even split of remaining traffic
Incremental upgrades and
better-than-proportional performance gain

## Slide 9: Roadmap
How do we wire servers to ToRs?
  Our wiring method uses incrementally deployable, short wires asdfasdasdgadsfgs
How can we use multiple ToRs?
  Our routing protocols increase the number of short paths and better balance the remaining load
What about the rest of the network?

## Slide 10: Roadmap
How do we wire servers to ToRs?
  Our wiring method uses incrementally deployable, short wires asdfasdasdgadsfgs
How can we use multiple ToRs?
  Our routing protocols increase the number of short paths and better balance the remaining load
What about the rest of the network?

## Slide 11: Subways Physical Topology
Notes: This is a diagram depicting 4 racks of servers wired exactly how they would be today…
rows
[point out that we take half of a rack and wire to left, half to bottom “bottom half is always connected to … top is always connected…”
That’s what gives us the zigzag pattern of subways
Now, obviously, we cant just keep extending this forever, so what do we do with the edges?
Well the solution is just to make a loop of racks by connecting racks across an aisle to a different row in the data center, like I’ve shown in the inset.
With this type of wiring pattern, servers are only connected to racks that are physically adjacent.
Thus wire lengths in Subways can be kept short.
Furthermore note that…
-not that hard. Literally right next to each other, if you cross over the top, everyone has short wires. Don’t see the paper, see the tech report for the broad set of options. I’d be happy to discuss this offline.

## Slide 12: Roadmap
How do we wire servers to ToRs?
  Our wiring method uses incrementally deployable, short wires asdfasdasdgadsfgs
How can we use multiple ToRs?
  Our routing protocols increase the number of short paths and better balance the remaining load
What about the rest of the network?

## Slide 13: Local Traffic
Always prefer shorter paths
Subways creates short paths to more nodes
  ⇒Less traffic in the oversubscribed network
Single link
or trunk
Subways

## Slide 14: Uniform Random
Simple
Doesn’t use capacity optimally if there are 2+ hot racks

## Slide 15: Uniform Random
Simple
Doesn’t use capacity optimally if there are 2+ hot racks

## Slide 16: Adaptive Load Balancing
Using either MPTCP or Weighted-ECMP
Spreads load more effectively

## Slide 17: Detours
Offload traffic to nearby ToRs
Detours can overcome oversubscription

## Slide 18: Roadmap
How do we wire servers to ToRs?
  Our wiring method uses incrementally deployable, short wires asdfasdasdgadsfgs
How can we use multiple ToRs?
  Our routing protocols take advantage of short paths and better balances the remaining load
What about the rest of the network?

## Slide 19: Wiring ToRs into the Backbone: Type 1
Wire all ToRs into the same cluster
Routing is unchanged
Cluster may need to be rewired

## Slide 20: Wiring ToRs into the Backbone: Type 2
Just like server-ToR, Cross-wire adjacent ToRs to different clusters
Incremental cluster deployment, short paths & stat muxing
Routing is more complex

## Slide 21: Evaluation

## Slide 22: Evaluation Methodology
Packet-level simulator
2 ports per server, 15 servers per rack
3 levels of 10 GbE switches
Validated using a small Cloudlab testbed

## Slide 23: How Does Subways Compare to Other Upgrade Paths?
Chart: Server Bandwidth
| 10G | 25G | 40G | 10G+10G | 10G+25G
Type 2 | 2.7082 | 4.9527
Type 2 w/ LB | 3.4212 | 5.7679
Type 2 w/ Detours | 3.924 | 5.903
Single Port | 1 | 2.4308 | 3.758
90 node MapReduce shuffle-like workload
For this workload, superlinear speedup

## Slide 24: Other Questions We Address
How sensitive is Subways to job size?
How sensitive is it to loop size?
Is it better than multihoming/MC-LAG?
How do performance effects scale with port count?
Does the degree of oversubscription have an effect on the benefits of Subways?
How much CPU overhead does detouring add?

## Slide 25: Subways
Wire multiple links to overlapping ToRs
Enables incremental upgrades
Short paths to more nodes
Better statistical multiplexing
Superlinear speedup depending on workload